LGR note: Updated for LEED v4 (May 25, 2016)

SECTION ###### - SECTION TITLE

GENERAL

RELATED DOCUMENTS

Plans and general provisions of the Contract, including but not limited to the Agreement and General Conditions and other Division 01 Specification Sections, apply to this Section.

DESCRIPTION OF WORK

Work Included:  Provide labor, materials and equipment necessary to complete the work of this Section, including but not limited to the following:

Insert description here.

Sustainable Design Intent:  Comply with project requirements intended to achieve sustainable design, measured and documented according to the LEED Green Building Rating System, of the US Green Building Council.  Refer to Section 018113 - SUSTAINABLE DESIGN AND LEED REQUIREMENTS, for certification level and certification requirements.

Related Work: The following items are not included in this Section and are specified under the designated Sections:

Section ###### - SECTION TITLE for whatever.

SUBMITTALS

Product Data:  For each type of product indicated.

LEED Submittals:

Credit MR 3 - 5, Building Product Disclosure and Optimization: To be determined.

Credit MR 3 Building Product Disclosure and Optimization, Environmental Product Declarations (EPD):

Credit MR 3, Option 1: For carpets, submit industry-wide EPDs.

Credit MR 3, Option 1: For gypsum board, carpets, submit product-specific Type III EPDs.

Credit MR 4 Building Product Disclosure and Optimization, Sourcing of Raw Materials:

General: For credit achievement calculation, submit location of products sourced (extracted, manufactured, and purchased), indicating number of miles from the project site.

Credit MR 4, Option 1: For carpets, submit corporate sustainability reports (CSR).

Credit MR 4, Option 2, Leadership Extraction Practices:

Extended Producer Responsibility: Only available for gypsum board, acoustical ceiling panels, and carpets.

Bio-Based Materials: Bio-based products must meet the Sustainable Agriculture Network’s Sustainable Agriculture Standard. Bio-based raw materials must be tested using ASTM Test Method D6866 and be legally harvested, as defined by the exporting and receiving country. Exclude hide products, such as leather and other animal skin material. Products meeting bio-based materials criteria are valued at 100% of their cost for the purposes of credit achievement calculation.

Wood Products: Wood products must be certified by the Forest Stewardship Council or USGBC-approved equivalent. Products meeting wood products criteria are valued at 100% of their cost for the purposes of credit achievement calculation.

Materials Reuse: Reuse includes salvaged, refurbished, or reused products. Products meeting materials reuse criteria are valued at 100% of their cost for the purposes of credit achievement calculation.

Recycled Content: Submit percentages by weight of postconsumer and preconsumer recycled content for products having recycled content.  Include statement indicating costs for each product having recycled content.

Credit MR 5 Building Product Disclosure and Optimization, Material Ingredients:

Credit MR 5, Option 1, Material Ingredient Reporting: For gypsum boards, carpets, submit Cradle to Cradle (C2C) certifications or Health Product Declarations (HPD).

Credit MR 5, Option 1: The end use product has been certified at the Cradle to Cradle v2 Basic level or Cradle to Cradle v3 Bronze level.

Credit MR 5, Option 1: The end use product has a published, complete Health Product Declaration with full disclosure of known hazards in compliance with the Health Product Declaration open Standard.

Credit MR 5, Option 2, Material Ingredient Optimization: For carpets, submit Cradle to Cradle (C2C) certifications.

Credit MR 5, Option 2: The end use product has been certified Cradle to Cradle (C2C) v2 Gold Platinum or v3 Silver Gold Platinum.

Option 3: Unavailable.

Credit EQ 2 Low-Emitting Materials, General Emissions Evaluation: Building products must be tested and determined compliant in accordance with California Department of Public Health (CDPH) Standard Method v1.1–2010, using the applicable exposure scenario.

For wet-applied products, submit volume used.

Credit EQ 2 Low-Emitting Materials, General Emissions Evaluation: Building products must be tested and determined compliant in accordance with California Department of Public Health (CDPH) Standard Method v1.1–2010, using the applicable exposure scenario.

For wood composite materials, submit test results, including TVOC emissions.

For adhesives, submit test results, including TVOC emissions and VOC content.

For gypsum board, submit GreenGuard certification.

For carpets, submit VOC content and Carpet and Rug Institute’s Green Label Plus certification.

For wet-applied products, submit volume used.

PRODUCTS

MANUFACTURERS

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

List manufacturers here, alphabetically.

PRODUCT

Forest Certification:  Provide doors made from wood products obtained from forests certified by an FSC-accredited certification body to comply with FSC 1.2, "Principles and Criteria."

Products:

Sustainable Design Requirements:  Provide carpet that complies with testing and product requirements of CRI Carpet and Rug Institute's "Green Label Plus" program.

ACCESSORIES

Adhesives:

VOC Limits:  Provide adhesives with VOC content not more than __ g/L when calculated according to 40 CFR 59, Subpart D (EPA method 24).

Methylene chloride and perchloroethylene may not be intentionally added to adhesives.

Do not use adhesives that contain urea formaldehyde.

Paints and Coatings:

VOC Limits:  Provide paints and coatings with VOC content not more than __ g/L when calculated according to 40 CFR 59, Subpart D (EPA method 24).

Methylene chloride and perchloroethylene may not be intentionally added to paints and coatings.

Sealants:

VOC Limits:  Provide sealants with VOC content not more than __ g/L when calculated according to 40 CFR 59, Subpart D (EPA method 24).

Methylene chloride and perchloroethylene may not be intentionally added to sealants.

EXECUTION

EXAMINATION

Examine substrates, . . . . .

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

INSTALLATION

FIELD QUALITY CONTROL

CLEANING AND PROTECTION

END OF SECTION